## Slide 1: Unicorn HAT & Minecraft Drawing to the real world

## Slide 2: Showing LEDs Getting started with the Unicorn HAT

## Slide 3
# Load Libraries
import time
import unicornhat as UH
for y in range(8):
for x in range(8):
UH.set_pixel(x, y, 150, 150, 150)
UH.show();
time.sleep(1)

## Slide 4: Minecraft to Unicorn HAT Mapping blocks to pixels

## Slide 5
#!/usr/bin/env python
# Load Libraries
import time
import mcpi.minecraft as minecraft
import mcpi.block as block
import unicornhat as UH
############ Write your program below #############
#Connect Minecraft API to the currently open world
mc = minecraft.Minecraft.create()
#draw canvas
mc.setBlocks(0,0,0, 7,64,7, 0)
mc.setBlocks(0,-1,0, 7,-1,7, 7)
#check canvas
while True:
for z in range(8):
for x in range(8):
#get the current block
block_type = mc.getBlock(x,0,z)
if block_type == 35:
UH.set_pixel(x, z, 100, 100, 100)
UH.show()
else:
UH.set_pixel(x, z, 0, 0, 0)
UH.show()

## Slide 6: Greyscale Differentiate block colour

## Slide 7
#!/usr/bin/env python
# Load Libraries
import time
import mcpi.minecraft as minecraft
import mcpi.block as block
import unicornhat as UH
############ Write your program below #############
#Connect Minecraft API to the currently open world
mc = minecraft.Minecraft.create()
#draw canvas
mc.setBlocks(0,0,0, 7,64,7, 0)
mc.setBlocks(0,-1,0, 7,-1,7, 7)
#check canvas
while True:
for z in range(8):
for x in range(8):
#get the current block
block = mc.getBlockWithData(x, 0, z)
block_type = block.id
if block_type == 35:
block_colour = block.data
if block_colour == 7:
UH.set_pixel(x, z, 50, 50, 50)
elif block_colour == 8:
UH.set_pixel(x, z, 100, 100, 100)
elif block_colour == 0:
UH.set_pixel(x, z, 150, 150, 150)
UH.show()
else:
UH.set_pixel(x, z, 0, 0, 0)
UH.show()

## Slide 8: Full Colour Add the rest of the colours